## Slide 1: IoT Practice-II Arduino Programming on WoW Kit (Others)

## Slide 2: 6. Ambient Light Sensor

## Slide 3: Ambient Light Sensor
GL10537-1 photoresistor
  CDS(Cadmium sulfide)
The larger the light is injected,
The smaller the resistance of CDS becomes.

## Slide 4: Ambient Light Sensor
GL10537-1 photoresistor

## Slide 5: Sample : Ambient Light Sensor
#define LIGHT A3
#define LED 9
void setup() {
Serial.begin(9600);
pinMode(LIGHT, INPUT);
pinMode(LED, OUTPUT);
}
void loop() {
int value = analogRead(LIGHT);
int data = map(value, 0, 1023, 1023, 0);
Serial.print("LIGHT : ");
Serial.println(data);
analogWrite(LED, value);
delay(100);
}
map(value, fromLow, fromHigh, toLow, toHigh);
// change the dynamic range of value

## Slide 6: LAB-6 : Ambient Light Sensor
Program the system satisfying the following specification
Spec.-1 : Design an obstacle detector which beeps a sound when an obstacle passes by
in front of photoresistor.
Spec.-2 : (optional)
Program the remote monitoring system of the amount of room’s ambient light
using IoTMakers cloud.

## Slide 7: 7. Ultrasonic Sensor

## Slide 8: Ultrasonic Sensor
HC-SR04
  Non-contact distance measurement
    2~400cm
    Measuring angle : 15 degrees
Procedure to measure the distance
  Using IO trigger for at least 10us high level signal.
  The Module automatically sends eight 40 kHz and detect whether there is a pulse signal back.
  If the signal back, through high level , time of high output IO duration is the time from sending ultrasonic to returning.
    Test distance = (high level time × velocity of sound (340M/S) / 2,

## Slide 9: Sample-I : Ultrasonic Sensor
pulsing(pin, pulse);
* Read a pulse on the pin.
void loop() {
long duration, distance;
digitalWrite(trigPin, LOW);
delayMicroseconds(2);
digitalWrite(trigPin, HIGH);
delayMicroseconds(10);
digitalWrite(trigPin, LOW);
duration = pulseIn(echoPin, HIGH);
distance = duration * 17 / 1000;
if (distance >= 200 || distance <= 0) {
Serial.println("Unable to measure distance");
} else {
Serial.print(distance);
Serial.println(" cm");
}
delay(500);
}
#define trigPin 13
#define echoPin 12
void setup() {
Serial.begin (9600);
pinMode(trigPin, OUTPUT);
pinMode(echoPin, INPUT);
}

## Slide 10: Sample-II : Ultrasonic Sensor with Warning
pulsing(pin, pulse);
* Read a pulse on the pin.
if (distance >= 200 || distance <= 0) {
Serial.println("Unable to measure distance");
} else {
Serial.print(distance);
Serial.println(" cm");
}
if(distance <= 20) {
tone(BUZZER, 600);
delay(distance * 10);
noTone(BUZZER);
delay(distance * 10);
} else {
delay(500);
}
}
#define trigPin 13
#define echoPin 12
void setup() {
Serial.begin (9600);
pinMode(trigPin, OUTPUT);
pinMode(echoPin, INPUT);
}
void loop() {
long duration, distance;
digitalWrite(trigPin, LOW);
delayMicroseconds(2);
digitalWrite(trigPin, HIGH);
delayMicroseconds(10);
digitalWrite(trigPin, LOW);
duration = pulseIn(echoPin, HIGH);
distance = duration * 17 / 1000;

## Slide 11: LAB-7 : Ultrasonic Sensor
Program the system satisfying the following specification
Spec.-1 : Design an obstacle detector which beeps a sound when an obstacle approaches less than 30cm.
Spec.-2 : (optional)
Create a level meter which shows the distance between the device
and obstacles with full-color LED. The brightness of LED depends on the amount of distance from obstacle. If the obstacle is far from the sensor,
the color of LED becomes darker.

## Slide 12: 8. Infrared Sensor

## Slide 13: Infrared Sensor
Sharp GP2Y0A21YK0F
  Distance measuring sensor unit
    10~80cm
  Composed of an integrated combination of position sensitive detector(PSD) and infrared emitting diode(IRED) and signal processing unit.
  The voltage output is corresponding to the detection distance.
  Also used as a proximity sensor.
  Application
    Touch-less switch (sanitary equipment, control of illumination)
    Robot cleaner
    Sensor for energy saving (ATM, Copier, Vending machine)
    Amusement equipment (Robot, Arcade game machine)

## Slide 14: Infrared Sensor
Block diagram of Sharp GP2Y0A21YK0F

## Slide 15: Infrared Sensor
Distance measuring characteristics of Sharp GP2Y0A21YK0F

## Slide 16: Sample-I : Infrared Sensor
int distance = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
int volt = map(analogRead(A0), 0, 1023, 0, 5000);
distance = (27.61 / (volt - 0.1696)) * 1000; // empirical equation
Serial.print(distance);
Serial.println(" cm");
delay(500);
}

## Slide 17: Sample-II : Infrared Sensor with Alarming
#define BUZZER 6
#define SIGNAL_PIN A0
int distance = 0;
void setup() {
Serial.begin(9600);
pinMode(BUZZER, OUTPUT);
pinMode(SIGNAL_PIN, INPUT);
}
void loop() {
int volt = map(analogRead(SIGNAL_PIN), 0, 1023, 0, 5000);
distance = (21.61 / (volt - 0.1696)) * 1000;
if(distance <= 20)
{
tone(BUZZER, 600);
delay(distance * 5);
noTone(BUZZER);
delay(distance * 5);
}
else
{
delay(500);
}
Serial.print(distance);
Serial.println(" cm");
delay(500);
}

## Slide 18: Sample-III : Infrared Sensor with IoTMakers
void init_iotmakers() {
while(1) {
Serial.print(F("Connect to AP..."));
while(g_im.begin(WIFI_SSID, WIFI_PASS) < 0) {
Serial.println(F("retrying"));
delay(100);
}
Serial.println(F("Success"));
g_im.init(deviceID, authnRqtNo, extrSysID);
Serial.print(F("Connect to platform..."));
while(g_im.connect() < 0) {
Serial.println(F("retrying."));
delay(100);
}
Serial.println(F("Success"));
Serial.print(F("Auth..."));
if(g_im.auth_device() >= 0) {
Serial.println(F("Success..."));
return;
}
}
}
#include <WiFi.h>
#include <IoTStarterKit_WiFi.h>
#include <OneWire.h>
IoTMakers g_im;
#define deviceID "{YOUR_DEVICE_ID}"
#define authnRqtNo "{YOUR_DEVICE_PASSWORD}"
#define extrSysID "{YOUR_GATEWAY_ID}"
#define WIFI_SSID "{WIFI_NAME}"
#define WIFI_PASS "{WIFI_PASSWORD}"
#define LIGHT A3
#define TAG_ID "LIGHT“ // be careful !

## Slide 19: Sample-III : Infrared Sensor with IoTMakers
void setup() {
Serial.begin(9600);
pinMode(LIGHT, INPUT);
init_iotmakers();
}
void loop() {
static unsigned long tick = millis();
if(g_im.isServerDisconnected() == 1) {
init_iotmakers();
}
if((millis() - tick) > 1000) {
send_temperature();
tick = millis();
}
g_im.loop();
}
int send_ambient_light()
{
int value = analogRead(LIGHT);
int data = map(value, 0, 1023, 1023, 0);
Serial.print("LIGHT : ");
Serial.println(data);
if(g_im.send_numdata(TAG_ID, (double)data) < 0) {
Serial.println(F("fail"));
return -1;
}
return 0;
}

## Slide 20: LAB-8 : Infrared Sensor
Program the system satisfying the following specification
Spec.-1 : Measure the distance between IR sensor and obstacles
at every 0.5 sec..
Spec.-2 : (optional) Calibrate the measurement by adjusting the coefficient
of equation. .

## Slide 21: 9. Servo Motor

## Slide 22: Servo Motor
SG90
  Operating Voltage is +5V typically
  Torque: 2.5kg/cm
  Operating speed is 0.1s/60°
  Gear Type: Plastic
  Rotation : 0°-180°
  Weight of motor : 9gm
Positioning of arm
  When on-time is
    1ms, the position of arm is 0 degree.
    1.5ms, 90 degree
    2ms, 180 degree
Torque of 2.5kg/cm

## Slide 23: Sample : Servo Motor
#include <Servo.h>
Servo myServo;
int angle = 0;
void setup() {
Serial.begin(9600);
myServo.attach(3);
}
void loop() {
// move from 0 to 180 degrees
for(angle = 0; angle < 180; angle++) {
myServo.write(angle);
delay(15);
}
// move in reverse direction, from 180 to 0 degrees
for(angle = 180; angle > 0; angle--) {
myServo.write(angle);
delay(15);
}
}

## Slide 24: LAB-9 : Servo Motor
Program the system satisfying the following specification
Spec.-1 : Calculate the average swing speed after measuring 10 times swings forward &
backward, and compare the value of datasheet (0.1s/60 degree).
* To measure the elapsed time, use millis() function.
Spec.-2 : (optional) Report the position of arm at every 0.5 sec. to IoTMakers.

## Slide 25: 10. Piezo Vibration Sensor

## Slide 26: Piezo Vibration Sensor
SEN0209
  Able to detect vibration, flexibility, impact and touch.
    Operating voltage : 5V
    Interface : Gravity PH2.0 3-pin interface
    Operating temperature : 0~85

## Slide 27: Sample-I : Piezo Vibration Sensor
#define VIB_SENSOR A0
void setup() {
// put your setup code here, to run once:
Serial.begin(9600);
pinMode(VIB_SENSOR, INPUT);
}
void loop() {
// put your main code here, to run repeatedly:
Serial.println(analogRead(VIB_SENSOR));
delay(100);
}

## Slide 28: Sample-II : Touch Switch with Piezo Vibration Sensor
#define VIB_SENSOR A0
void setup() {
// put your setup code here, to run once:
Serial.begin(9600);
pinMode(VIB_SENSOR, INPUT);
}
void loop() {
// put your main code here, to run repeatedly:
Serial.println(analogRead(VIB_SENSOR));
delay(100);
}
#define VIB_SENSOR A0
#define TOUCH 1
void setup() {
// put your setup code here, to run once:
Serial.begin(9600);
pinMode(VIB_SENSOR, INPUT);
}
void loop() {
// put your main code here, to run repeatedly:
int isTouch = digitalRead(VIB_SENSOR);
if(isTouch == TOUCH)
Serial.println("TOUCH");
delay(100);
}

## Slide 29: LAB-10 : Piezo Vibration Sensor
Program the system satisfying the following specification
Spec.-1 : Display the measured analog level, at which Sample-II code detects touching.
Spec.-2 : (optional)
Upload the measured analog output to IoTMakers.

## Slide 30: Q&A