## Slide 1: IoT Practice-III Raspberry Pi 3 B as IoT Gateway (Embedded System)

## Slide 2: Agenda
Introduction to Embedded System
Embedded Platform
ARM Processor
Linux
System Development (ARM+Linux)
Bootloader
Kernel Configuration
File System (Ramdisk)
Module Programming
Device Driver

## Slide 3: Introduction to Embedded System

## Slide 4: What’s Embedded System ?
All kinds of digital systems embedding micro-processor
  performing the functions specific to an application.
  optimized to the specific design goal.
Comparison with the conventional system
  Stand-alone computer vs. Computer embedded in Product
  General Purpose Computer vs. Special Purpose Computer

## Slide 5: Why Embedded System ?
Paradigm of digital system design paradigm has changed rapidly.
H/W-Only
(ASIC)
S/W-Only
H/W-SW Co-design
Standalone
(Firmware)
OS-Mounted
High performance
Flexibility for adopting rapid upgrading& updating)
Complicated Function
Multitasking
Various types of networking
Efficient HW resource management

## Slide 6: Design Aspects of Embedded System
Design goal
  High performance : real-time operation is required
  Flexibility : easy to modify & upgrade.
Design methodology
  A co-design of hardware and software to perform the specific function optimally.
Difficulty
  Not easy to co-design HW & SW
  Requires high-level design expertise

## Slide 7: Design Considerations
Resource limitation
  Constrained memory usage
  Software customization : reduction of code size, high performance coding
Portability
  Small-sized : small packages
  Battery operated : low power consumption
Short life-cycle of product
  Easy to upgrade : flexible system
Low cost
  Low material cost : survey on available chips, maintain supply-chain
  Low design cost : design automation
Design goal of : Trade-offs between design considerations

## Slide 8: Construction of Embedded System
Hardware components
  Processor
  Peripheral devices
  Embedded hardware platform = Processor + Peripherals
Software components
  System software
  Middle-ware
  Application software
Development tools

## Slide 9: HW Components - Processor
Micro processing unit (MPU)
  Computation-bound
Micro controller unit (MCU)
  Control-bound
Digital signal processor (DSP)
  Specialized for processing digital signals such as audio, video, …
Application specific processor (ASP) :
  Java processor
  Network processor
  Crypto processor
  Reconfigurable processor

## Slide 10: HW Components – Peripherals
Peripheral devices
  Perform a special I/O function or data processing task in order to speed up overall system’s throughput & reduce CPU’s load.
ASSP device
  Off-the-shelf product designed to perform a specific function.
    network controller, video codec, USB controller, etc
ASIC device
  Self-developed, field-programmed
  High-cost & high-speed
  Fully customized

## Slide 11: SW Components
System software
  Operating system
  Device driver
Middle-ware
  Application specific libraries
  Multimedia, Java, etc
Application software
  What you want to do

## Slide 12: Development Tools
SW Development tools
  Compiler, linker, debugger, std. library,
  In-system programmer
HW development tools
  PCB artwork & analysis : thermal, vibration, fatigue life, convective air flow, stress, harness
Commercial vs. Free-ware
  Development cost
  Technical support
  Continuous maintenance
  Reliability

## Slide 13: Theoretical Flow of Co-Design
System Specification
Partition
Design constraints & Operating condition
Hardware Description Language
High-level Programming Language
System Description Language
Cost function
Hardware Synthesis
Compilation
RTL description
Machine code
NV memory (Code)
ASIC
uP + Memory + I/O’s
SoC, SoB
Co-simulation
Co-verification
Design Cost Prediction
& Design Space Exploration
Automated Design

## Slide 14: Practical Flow of Co-Design
Design Specification
Partition
Micro-Processor Selection
Bootloader/Startup
Designer’s Expertise
& Intuition
Peripheral Devices Selection (ASIC/ASSP)
HW Platform Design
OS Kernel
Customization
Device Driver
Application
Application
HW
SW
OS-mount
Standalone

## Slide 15: Embedded Platform

## Slide 16: Embedded Platform
The base platform in which HW and SW components are integrated.
  Self-developed or ready-made

## Slide 17: Hardware Platform Design
Embedded processor selection
  Processor type : MPU, MCU, DSP, ASIP
  Instruction set architecture : RISC, CISC
  Processor architecture
    Von Neumann, Harvard
    DSP-features : Dual-memory access, MAC, Floating-point
  Memory : Flash, DRAM/SRAM
Application specific peripheral devices
  On-chip : integrated in processor
  Off-chip
    Rapid prototyping : EPLD, FPGA, ….
    ASSP : Ethernet, USB, PCMCIA, LCD, Audio codec, Touch-screen, ….
Hardware implementation
  System-on-Board (SoB) : On-PCB
  System-on-Chip (SoC) : One-Chip
Micro-processor
ROM
RAM
I/O
I/O
I/O
SoB/SoC

## Slide 18: Embedded Processor
Intel
  x86 (386, 486, Pentium)
ARM
  ARM7, ARM9, StrongARM, ARM10, ARM11
Motorola
  PowerPC, 68K / ColdFire, Mcore, Dragon Ball
MIPS Technologies
  MIPS32 4K, 5K
Hitachi
  Super-H (SH-1, SH-2, SH-3, SH-4, SH-5)
Texas Instrument
  TMS320 (DSP), TMS370 / MSP430 (MCU)

## Slide 19: Typical Design Procedure of Embedded System
Prepare boot-up program
  Initialize the hardware : POST, setup parameters, checking its functionality.
  Boot operating system
Select operation system
  customize OS kernel
Setup the development environment
  Tool chain : Compiler / Debugger / In-circuit programmer
  Processor-dependent
Develop device drivers if need.
  depends on OS & the types of peripheral devices
  Read-made or self-developed

## Slide 20: Typical Design Procedure of Embedded System
Check Libraries, APIs
  Middle ware
    Functional libraries for the specific application domain
    Support application software development
  Human interface : CLI (command-line interface) or GUI
Program Application Software
  Handheld devices : PDA, Cellular/Smart phone, MP3 Player, PMP, Game console
  Internet appliances,
  Factory automation, Office automation
  Automotive appliance : Car navigation, ECU
  Ubiquitous, wearable computing
  Sensor network

## Slide 21: Embedded Operating System
Needs for OS
  Multitasking
  High-functionalities
    Networking & support multimedia
    Limitation of sequential programming
    Support & manage various types of i/o devices
  Rapid development and Maintenance
    Easy to modify & download SW for changing new requirements from user & market
    Provide new creative & high-quality solutions in time

## Slide 22: Embedded Operating System
Linux
Window CE Embedded
VxWorks / pSOS : real-time OS
PalmOS : PDA
NetBSD : used widely for comm. system
eCOS : open source. Non-linux
Commercial vs. Free
  License policy

## Slide 23: ARM + Linux Platform
Most widely used embedded platform
  Processor : ARM processor
  OS : Linux
Legendary platforms
  Assabet : Intel SA-1110 evaluation board
  LART (Linux Advanced Radio Terminal) : Delft Univ. of Tech. (Netherlands)
  PLEB : Univ. of New South Wales (Australia)
  Itsy : DEC (Compaq) Western Research Lab
  NetWinder : Corel Computer
  Others

## Slide 24: ARM Processor
32-bit processor families from ARM Inc.
  Low-power / High-performance
  The most widely used 32-bit micro-processor
ARM : www.arm.com
  ARM : Advanced RISC Machine
  Established in 1990.11 as joint venture (England)
  Fund : Apple Computer, VLSI Technology
  Technology : Acorn Computer Group
  Provide IP (Intellectual Property) of ARM ISA

## Slide 25: ARM Processor
Markets for ARM in 2012 & 2017
CAGR : Compound Annual Growth Rate

## Slide 26: ARM Processor
Single-core performance based on SPECINT2k6.

## Slide 27: ARM Processor
ARM instruction set architecture

## Slide 28: ARM Processor
Performance of ARM family in DMIPS/MHz

## Slide 29: Linux
Linux overview
  Started by Linus B. Torvals
  A clone of UNIX
  Free : Copyright  Copyleft
Kernel release
  First version : 0.01, (1991)
  www.kernel.org
Numbering Linux version
  (major).(minor).(patch level)
  Minor :
    Even : stable release
    Odd : development release
  Latest stable version : 2.6.28

## Slide 30: Linux
Strong point
  Free : Open source, low design cost
  Open architecture : support various processor
  Large development people
    Short development time
    Easy to obtain device drivers
  Stable : UNIX clone
Weak point
  Difficult to design
  Weak to GUI, Web brwosing, multimedia function

## Slide 31: ARM Processor

## Slide 32: ARM Processor
32-bit RISC processor
Load-store architecture
Fixed instruction length
  16-bit : Thumb instructon set
  32-bit : ARM instruction set

## Slide 33: ARM Core
ARM Core
  the micro-architecture which can execute ARM instruction set architecture (ISA).
  Its performance depends on the pipeline architecture & data-path structure.
  Semiconductor foundry make its own ARM processors by adding memory and peripheral devices on ARM core.
System core
  ARM core + memory unit (buffer, cache, MMU, MPU)
  Determine the structure & performance of ARM processor
Type of ARM core
  Hard macro-cell
    Core in layout level, so any design change is not allowed.
    Core size & supply voltage is fixed by ARM.
  Synthesizable core
    HDL description of core in register-transfer-level.
    Any change on core size or memory structure is allowed, but not for functionality
    -S suffix : ARMT7TMDI-S, ARM926EJ-S, ARM1136J-S

## Slide 34: ARM Instruction Set Architecture
Features of ARM ISA
  All instructions are conditional
  Shift & ALU by one instruction
  Auto-increment & decrement
  Multiple registers read/write
  16-bit instruction mode

## Slide 35: ARM Instruction Set Architecture
Suffix of ARM
  T : Thumb
  E : DSP extension
  J : Java extension (Jazelle)
  Z : TrustZone,
  T2 : Thumb-2, Blend 16-/32bit instruction.
    25% faster than 16-bit, 26% smaller than 32-bit
  TDMI : T(Thumb), D(Debug), M(Multiplier, 64-bit result), I (In-circuit emulation interface)
  F : Vector floating point coprocessor
  MP : multi-processor
  S : Synthesizable core
TCM : Tightly Coupled Memory
ABI : AHB (AMBA Advanced High-performance Bus) Bus Interface. On-chip bus spec. for interconnection and management of function blocks for SoC.
Cortex : Thumb-2 ISA. 65 % faster interrupt handling. A-series (application), R-series (Real-time), M-series (Microcontroller). 3-stage pipeline, Harvard architecture. Accelerate the move from legacy 8-/16-bit architecture to 32-bit

## Slide 36: ARM Operating Mode of ARM
6 privileged modes + 1 user mode
Privileged mode
  System mode : run privileged operating system tasks
  Supervisor mode : protected mode for operating system, entered by reset, software interrupt
  FIQ mode : entered by fast interrupt (FIQ), high-speed data transfer or channel process
  IRQ mode : entered by normal interrupt, general purpose interrupt handling
  Abort mode : entered by pre-fetch abort, data abort exception, virtual memory / memory protection, used to handle memory access violations.
  Undefined mode : entered by undefined instruction exception, used to handle undefined instructions. software emulation of hardware coprocessors

## Slide 37: Operating Mode of ARM
User mode
  Normal program execution mode.
  Unable to access protected system resource, or change mode
Exception mode
  Entered by hardware or software exception
  Has banked register set (stack pointer, link register, status register) to minimize exception handling latency
  Access system resource
  Able to change operating mode,

## Slide 38: Processor Operating State
2 operating states
  ARM state, Thumb state
ARM state
  execute 32-bit instruction set
Thumb state
  execute 16-bit instruction set
State transition
  By special instruction (BX)
  T-bit in program status registers

## Slide 39: ARM Register Set
37 registers
  31 general purpose registers
  6 status registers
Only 16 registers of 31 GPRs are visible : R0 ~ R15
  R13 : stack pointer
  R14 : link register, branch & link (BL) instruction
  R15 : program counter
Status register
  CPSR (current program status register)
  5 SPSR (saved program status register)
Register banking
  R0 ~ R7 : unbanked
  Depends on operating mode
    R8 ~ R12 : banked only in FIQ mode
    R13 ~R14 : banked in exception mode

## Slide 40: Register Map
Banked
register

## Slide 41: Program Status Register
Condition code : Negative (N), Zero (Z), Carry (C), Overflow (V)
I : IRQ disable
F : FIQ disable
T : Thumb mode
M[4:0] : operating mode,
User (10000), FIQ (10001), IRQ (10010),
Supervisor (10011), Abort (10111), Undefined (11011),
System (11111)

## Slide 42: Exception of ARM
Reset
  When reset input is asserted
  Enter into Supervisor mode
Data Abort
  Data access memory abort
  By accessing invalid address
  Can be used by MMU or MPU to set MMU control register.
FIQ
  By asserting external FIQ input
  Interrupt which minimizes the interrupt processing time
  Because the exception vector entry for FIQ handler is located at the highest address, the handler can be loaded directly at the exception vector table entry without branching.
  Additional banking of R8~R14.

## Slide 43: Exception of ARM
IRQ exception
  By asserting external IRQ input
Pre-fetch abort exception
  Instruction fetch memory abort
  Used to handle BKPT (breakpoint) instruction in v5T ISA.
Undefined exception
  Any attempt to execute undefined instruction
  Used for software emulation of coprocessor & extension of instruction set
Software interrupt exception
  Execution of SWI instruction
  Enter into supervisor mode
  SWI type parameter : 24-bit in ARM mode, 8-bit in Thumb mode

## Slide 44: Exception of ARM
Recognition time of exception
  The end of execution of the current instruction
Exception vector table

## Slide 45: Procedure of Exception Handling
main()
woo()
ex_handler0()
Function call
exception
ex_handler1()
Nested exception
Program memory
0x 0000 0000
0x 0000 0004
Exception
vector
table
Exception vector
PC
IRQ
Trap
handler
JMP

## Slide 46: Exception Handling
Register changing
  When exception occurs, r3, r14, CPSR are banked
  The address value of link register depends on exception type
    Before return, the return address should be adjusted

## Slide 47: Exception Handling
Handler example

## Slide 48: Memory Format
ARM processor supports Little-endian, Big-endian memory access.
Data type : byte (8-bit), Half-word (16-bit), word (32-bit)
  Half-word : 2-byte boundary
  Word : 4-byte boundary

## Slide 49: APCS (ARM Procedure Call Standard)
Compiler is recommended to follow APCS
The interface between HPL and assembly language keeps APCS

## Slide 50: Linux

## Slide 51: Operating System
Role of OS
  Control & manage computing resource (CPU, memory, i/o).
  Provide execution environment for application program
  Support user interface : CLI, GUI
App1
System Call Interface
Kernel Core
Hardware
Device Driver
App2
App3
User space
Kernel space

## Slide 52: Kernel of Operating System
Kernel
  Essential part of operating system
  Control computing resource & execute the command that user issued
Kernel component
  Scheduler : share processor among multiple processes
  Memory management system : manage process address space
  Interrupt handler : service interrupt request
  System service : networking, interprocess communication
Kernel architecture
  Monolithic kernel
  Micro kernel

## Slide 53: Monolithic-kernel vs. Micro-kernel
(b) Micro kernel
  (a) Monolithic kernel
System Service API
Hardware
Integrated Kernel Architecture
1
n
2
System Service API
Hardware
Micro Kernel Architecture
1
n
2
Service Server

## Slide 54: Monolithic Kernel
Integrated all kernel functions into one kernel
Access kernel by calling kernel functions
Merit
  Simple implementation
  Manage system resources more effective
Demerit
  Low portability
  When kernel expands, increase kernel size & not easy to manage it
    Introduce module concept
Sample OS
  Unix (Solaris, HP-UX), Linux, Windows

## Slide 55: Micro Kernel
Keep only essential functions in kernel and divide other kernel functions into several server modules
Merit
  Easy to expand kernel function
  High portability
Demerit
  Complex to implement
  Overhead of message passing between server modules
  Low utilization of system resources
Sample OS
  Cray UNICOS/mk, CMU Mach OS, Sunsoft Chorus, Digital UNIX, Linux Mk, Hurd

## Slide 56: Kernel Components
Process management
  Process generation & termination
  Process communication : signal, pipe
  CPU scheduling, synchronization
  Access management of multiple processes on the limited resources.
Memory management
  Virtual memory management
  Effective memory hardware management by paging
  Stable system by memory protection between processes
Network management
  Support communication protocol
  Network routing & address resolution
  Manage network controller

## Slide 57: Kernel Components
File system management
  Support various file system by virtual file system (VFS)
  Represent physical structure of hard disk with logical structure
  File, directory management : normal file, device file, pipe
  Manage buffer cache for block I/O
Device management
  Verify & schedule I/O request
  Data transfer between peripherals and memory
  Manage device controllers
  Handle interrupt request

## Slide 58: Why Linux ?
No payment for use
  GNU Public License
  Save BOM (bill of materials) & development cost possibly
Many technical resources over internet
  Kernel sources
  documentations
  know-how’s
Support from a lot of communities and volunteers
  Free of technical supports
Demerit
  No guarantees of quality of support
  Originally designed for general-purpose, not for embedded (special purposed, real-time)

## Slide 59: Features of Linux Kernel
Multi-tasking, multi-user system
  based on time-division multi-plexing, multiple process can be executed, and multiple users can be logged on the same machine.
Symmetric multi-processor system
  support multiple same kinds of processors in one machine.
Multi-platform
  support various types of HW platform such as Intel IA-32, Alpha, Sparc, PowerPC, ARM, MIPS etc.
POSIX (portable operating system interface)
  compatible with UNIX standard interface.

## Slide 60: Features of Linux Kernel
Paging
  assign & swap the memory in pages.
System-V IPC support
  support System-V IPC such as semaphore, message queue, shared memory, etc.
Various types of file system support
  support FAT, VFAT, NTFS, ISO9660, Joilet as well as the default file system, ext2
Various execution file-format support
  a.out, ELF (executable and linking format).

## Slide 61: Features of Linux Kernel
Networking
  TCP/IP, IPX/SPX, Appletalk, SLIP (serial line IP), PPP. BSD socket.
Shared library
  Provide the program codes common to application programs in the form of shared library.
Module
  Add the device driver programs for new devices & new kernel functions dynamically to the existing kernel.
Support a lot of types of peripheral devices
  Network card, video card, sound card, CD-ROM, SCSI, USB, PCMCIA, IrDA, etc.

## Slide 62: Program Operating Mode
User mode
  Normal program is executed in user address space
Kernel mode
  Protected mode, privileged mode, supervisor mode
    Control accesses on system resource
  Exception handling
Mode change
  Change user mode to kernel mode
    By system call, exception
User Mode
Kernel Mode
System Call &
Interrupt
(trap, IRQ)

## Slide 63: Kernel Source
Source tree of Linux kernel
LINUX
Modules
mm
net
kernel
init
lib
include
lpc
unix
inet
fs
arch
drivers
mips
alpha
sparc
ppc
i386
net
char
block
scsi
sound
asm-alpha
linux
asm-i386
asm-m88k
asm-generic
asm-mips
asm-sparc
ext
ext2
xiafs
lsofs
hpfs
unsdos
nfs
proc
minix
msdos
sysv
kernel
boot
mm
math-emu

## Slide 64: Kernel Source
Documentation
Header files
  include/linux : common header file for Linux kernel
  include/asm : architecture-dependent header file, symbolic link
Architecture-independent source
  init : kernel booting related. Initialization code.
  kernel : essential part of kernel such as process management, timer, interrupt, signal, module, etc
  ipc : inter-process communication. Pipe, signal, socket, message passing, shared memory
  fs : file-system management source
  net : network related source
  drivers : device driver source
  lib : library function. In kernel, standard C library is not used.

## Slide 65: Kernel Source
Architecture-dependent source
  arch/i386/boot
  arch/i386/kernel
  arch/i386/mm
  arch/i386/lib
  arch/i386/math-emu
    if the floating-point coprocessor is not used, emulator related source
Source tree of kernel is different slightly on versions or packages

## Slide 66: Linux Kernel Image
Kernel image
  Execution file of Linux kernel
vmlinux
  Uncompressed kernel image
zImage
  Compressed kernel image under 1MB
bzImage
  Compressed kernel image
  Vmliux + initialization code (bootsect.S, setup) + bzImage attribute information

## Slide 67: Example of Kernel Compile
Download kernel source
  www.kernel.org : kernel source, patch file, ex) linux-2.4.0.tar.gz
> cd /usr/src
> rm –f linux
> tar zxvf linux-2.4.0.tart.gz
> mv linux linux-2.4.0
> ln –s lnux-2.4.0 linux
(patching)
> gzip –cd patch-2.4.1.gz | patch –p0

## Slide 68: Example of Kernel Compile
Kernel source directory : /usr/src/linux
Kernel configuration
Dependency check and generate kernel image & module
> make config / menuconfig / xconfig
> make dep
> make zImage
> make modules
> make modules_install

## Slide 69: Kernel Booting
Diskette booting
LILO (linux loader) booting
> dd if=bzimage of=/dev/fd0
> rdev –R /dev/fd0 /dev/hda1
> cp arch/i386/boot/bzimage /boot/vmlinuz-2.4.0
> cp system.map /boot/System.map-2.4.0
> vi /etc/lilo.conf
(editing)
image = /boot/vmlinuz-2.4.0
label=linux-2.4.0
root=/dev/hda1
read-only

## Slide 70: Cross-Development Environment

## Slide 71: ARM Development Tools
RVDS (RealView Development Suite) 4.0
  Commercial tools provided by ARM
    RVCT : RealView Compilation Tool
    IDE : ARM Workbench
    RealView ICE / Multi-ICE
    RealView ARMulator
TRACE32-ICD
  Commercial JTAG debugger for ARM, provided by Lauterbach, Germany
GNU tool-chain
  Compiler (gcc), C-library (glibc), binary utility (binutils)
JTAG dongle
  Flash memory fusing

## Slide 72: Cross-Development
Cross-Development
  Development machine != Execution machine
    Development machine  host computer
    Execution machine  target board
Procedure of cross-development
  Setup cross-development environment
  Preparing OS
  Developing device driver if need
  Programming application

## Slide 73: Detailed X-development Procedure
Detailed procedure for ARM + Linux platform
  Preparing cross-development environment
    Tool-chain : editor, compiler, debugger
    Flash memory fusing : JTAG
  Preparing OS
    Customizing boot loader
    Reconfiguring Linux kernel
    Creating or updating file system
      Memory file-system : ramdisk
      flash file-system
  Developing device driver
    Module programming
  Building up application program
    Install middle-ware if need

## Slide 74: Development Environment Setup
Host computer
  Edit, compile, debug the software for target board
Target board
  What we want to build
Connection between host computer & target board
  Serial port : connect target board’s consol port to host computer
  JTAG : program download & debug
  Ethernet : networking, file transfer, file system sharing
Serial
JTAG
Ethernet

## Slide 75: Host Computer Setup
Host computer provides software development environment for target board
Development tools installed in host computer
  Terminal emulator
  Tool-chain : editor, cross-compiler, debugger
  BOOTP server, TFTP server, NFS server
HUB
Target Board
Host Computer (LINUX)
Ethernet
Tool-chain
BOOTP Server
TFTP Server
NFS Server
Terminal Emulator
Serial
JTAG

## Slide 76: Terminal Emulator
Terminal emulator
  The program installed in host computer, which implements the functions of terminal using serial communication
  Play the role of the monitor & keyboard of target board console
  File upload & download
Hyper-terminal (Windows), minicom (Linux)
Terminal Emulator
Console
Host Computer
Target Board
File Upload
File Download
Serial interface program
Serial
Port
Console
Port

## Slide 77: BOOTP Server
bootp (Boot Protocol)
  Autobooting protocol of diskless client over IP network
  Use UDP protocol
  Assign IP address of target board through IP network
BOOTP Server
Bootp
Request
packet
Host PC
Target Board
IP address
In Bootloader
# bootp
TCP
/IP
TCP
/IP
daemon | Configuration file
xinetd | /etc/services /etc/xinetd.conf /etc/xinetd.d/bootp
bootpd | /etc/bootptab /etc/hosts

## Slide 78: TFTP Server
TFTP (Trivial File Transfer Protocol)
  Simple file transfer protocol using UDP
  Fast download of large data file (kernel image, ramdisk image, applicaions)
TFTP Server
RRQ
Host PC
Target Board
Kernel, ramdisk,
Bootloader
#tftp [file_name]
TCP
/IP
TCP
/IP
xinetd | /etc/services /etc/xinetd.conf /etc/xinetd.d/tftp
in.tftpd | /tftpboot

## Slide 79: NFS Server
NFS (Network File System)
  File-system sharing via network
  Provide storage space to target board
  Direct execution of cross-compiled result without trasnfering it to target board
/mnt
/nfs_resource
HUB
Target Board
Host Computer
HUB
Network File System
NFS server
NFS client

## Slide 80: Tool Chain
Tool chain
  A group of tools for the developments of system program & application program
  Text editor (vi), compiler (gcc), assembler (gas), linker (ld), utility programs (binutils), libraries (glibc)
Types of compilation
  Native compile : the processor executing compiler is same as the prcessor executing compiled result (executable file)
  Cross compile) : the processor executing compiler is different from the prcessor executing compiled result (executable file)
Compilation in embedde system development
  Cross compile

## Slide 81: Cross Tool Chain for ARM
Tool | Description
arm-linux-gcc | C compiler
arm-linux-c++ | C++ compiler
arm-linux-as | GNU assembler
arm-linux-gasp | GNU assembly preprocessor
arm-linux-ld | GNU linker
arm-linux-ar | Archives generation & modification
arm-linux-objdump | Get information about object file
arm-linux-nm | Display symbol information of objective file
arm-linux-strip | Delete symbol information from objective file
arm-linux-objcopy | Copy objective file
arm-linux-ranlib | Generate archive index
arm-linux-size | Display the size of sections of objective file
arm-linux-strings | Display strings & printable characters
arm-linux-addr2line | Translate address into file name and line number

## Slide 82: Make Utility
Utility program which compile efficiently multiple files
Control the sequence of compilation
Manage the location of program installation
“Makefile”
  Script file defining the compile procedure of make utility
  Consist of dependencies & rules

## Slide 83: Make Utility
(Makefile)
all: myapp
CC = gcc
INSTDIR = /usr/local/bin
CFLAGS = -g –Wall
myapp: main.o foo.o boo.o
$(CC) –o myapp main.o foo.o boo.o
main.o : main.c myhead.h
$(CC) $(CFLAGS) –c main.c
foo.o: foo.c foohead.h
$(CC) $(CFLAGS) –c foo.c
boo.o: boo.c boohead.h
$(CC) $(CFLAGS) –c boo.c
clean:
rm main.o foo.o boo.o

## Slide 84: GDB : GNU Debugger
GDB
  Text-based GNU debugger
  Default Linux debugger
How to use
  Use “–g” option when comple
  Execute GDB command “gdb [object_file_name]”
GDB commands
  run, backtrace, help, print, list, quit, break, clear, display, commnads, info, cont

## Slide 85: JTAG
JTAG
  Joint Test Access Group’s boundary scan for PCB and chip test
  1990 : adopted as IEEE 1149.1 standard
5-pin interface
  TDI : test data in
  TDO : test data out
  TCK : test clock input
  TMS : test mode select
  TRST : test reset

## Slide 86: JTAG Registers - 1
Identification register
  32-bit, JTAG ID code
    0 : Constant, ‘1’ if ID register exists
    1..11 : Manufacturer ID, “000 0000 1001”
    12..27 : Part Number, “1001 0010 0110 0001”
    28..31 : Stepping, “xxxx”

## Slide 87: JTAG Registers - 2
Instruction register
  4-bit, 5-bit (for SA1110), holding instruction
    1111 : BYPASS, TDI + Bypass + TDO
    00110 : IDCODE, TDI + ID register + TDO
    00011 : SAMPLE, TDI + boundary cells + TDO, sampling internal signals
    01001 : INTEST, TDI + boundary cells + TDO, internal test
    00000 : EXTEST, TDI + boundary cells + TDO, external test
    00101 : HIGHZ, external output pins = high-Z
Bypass register : 1-bit

## Slide 88: Boundary Scan Register
Boundary scan register
  PI : parallel input
  PO : parallel output
  SI : serial input
  SO : serial output

## Slide 89: Boundary Scan Chain
Chain of boundary scan registers

## Slide 90: External Connection of JTAG
External connection
External connectivity test

## Slide 91: TAP Controller
TAP controller : FSM that controls JTAG interface
  TMS is used to change state of TAPC

## Slide 92: TAP Controller
States of TAP controller
  Test-Logic-Reset : initialize TAPC
  Run-Test/Idle : ready to test
  Select DR-scan : connect scan cells
  Capture DR : capture the data of PI
  Shift DR : shift the data of scan cell, output to SO
  Update DR : output to PO
  Select IR-Scan : select IR
  Capture IR : output PI of IR to shift cell
  Shift IR : shift out the content of IR
  Update IR : output to PO

## Slide 93: State Transition Diagram of TAPC

## Slide 94: Flash Fusing
In-system flash memory fusing
  Programmed using JTAG
  Flash program utility : jflash
Example of flash memory map
Boot loader
0x0000 0000 ~
kernel (0x10 0000)
0x000c 0000 ~ 0x001c 0000
RAMdisk
0x0020 0000 ~
User space (/usr)
0x90 0000 – 0xa160 0000
Env. Values (0x10 0000)
0x0008 0000 ~ 0x000c 0000

## Slide 95: Flash Fusing
TCP/IP
Target Board
Host Computer
TFTP
Jflash cmd
boot loader
kernel
ramdisk
User Space
Parallel
port
JTAG
DRAM
command

## Slide 96: Bootloader

## Slide 97: What happened before main() ?
Preparing execution environment of main()
  Setup interrupt vector table
  Initialize the hardware components
  Load execution image (code, data)
  Preparing C-execution
    Set stack pointer properly
  Call main()
C runtime libarary
  crt0, crt1, …
Startup Code
Bootloader

## Slide 98: Bootloader
Bootloader
  The first program after system reset.
  System initialization
  Loading operating system into main memory
Characteristics of bootloader for embedded system
  Specific to a target OS
  Operate on flash memory
  Support commands for system development
    setip, bootp, tftp, flash, etc.

## Slide 99: Bootloader
Function of bootloader
  Hardware initialization
    CPU clock, memory interface, i/o port setting, network setting
  Memory copy
    From flash memory to RAM
    bootloader, kernel image, ramdisk image
  Supporting bootloader commands
  Booting OS kernel

## Slide 100: Bootloader
Procedure of bootloader
  start.S (assembly)  main.c (C language)
Start.S
  Interrupt vector table setting
  CPU setting
  GPIO setting
  Setup memory interface
  Copy bootloader itself from flash memory to RAM
  Stack pointer setting
  Handover control to bootloader in RAM

## Slide 101: Bootloader
main.c
  Initialize serial port (console)
  Initialize Ethernet port
  Copy kernel image & ramdisk image from flash to RAM
  Select booting mode (command mode or auto-boot)
    In command mode, handle the commands typed-in

## Slide 102: Operation Flow of Sample Bootloader
Set Interrupt handler
Interrupt masking
  ICMR (0x9005_0004) = 0x00
Prevent entering sleep mode
  PMCR (0x9002_0000) = 0x00
CPU clock setting
  PPCR (0x9002_0014) = 0x0A
Setup GPIO
  GPDR (0x9004_0004) = 0x0000_00FF
  GPSR (0x9004_0008) = 0x0000_00FF
  GRER (0x9004_0010) = 0x0000_0200
  GFER (0x9004_0014) = 0x0000_0000
Setup SDRAM parameters

## Slide 103: Operation Flow of Sample Bootloader
Call BeforeMain
  Copy bootloader itself to main memory.
  Call CMain function
Call CMain
  Set baud rate of serial port & download speed
  Initialize the timer & Ethernet interface
  Wait key-stroke
    Any key-stroke : enter bootloader command mode
    No key-stroke : auto-booting

## Slide 104: Source of Sample Bootloader (start.S)
.text
// vector table
// Reset = 0x0000 0000
// Undefined instruction = 0x0000 0004
// Software interrupt = 0x0000 0008
// Abort prefetch = 0x0000 000C
// Abort data = 0x0000 0010
// Not used = 0x0000 0014
// IRQ = 0x0000 0018
// FIQ = 0x0000 001C
.globl _start
_start: b reset
b undefined_instruction
b software_interrupt
b abort_prefetch
b abort_data
nop
b irq
b fiq
start.s

## Slide 105: Source of Sample Bootloader
reset:
// All interrupt disable. mask ALL interrupts.
// ICMR (interrupt control mask register) = 0x9005 0004
// IM[31:0] = ICMR[31:0], 0 (masked), 1 (enabled)
mov r1, #0x90000000
add r1, r1, #0x50000
mov r2, #0x00
str r2, [r1, #0x4]
// Protect enterting sleep mode
// PMCR(power management control register) = 0x9002 0000
// SF-bit = PMCR[0]
// 0 (Don't force invocation of sleep mode)
// 1 (Force invocation of sleep mode)
mov r1, #0x90000000
add r1, r1, #0x20000
mov r2, #0x00
str r2, [r1, #0x00]

## Slide 106: Source of Sample Bootloader
// PPCR(power manager PLL configuration register) = 0x9002 0014
// CPU clock = 206 MHz
// CCF 4..0 = PPCR[4:0]
// 00000 = 59.0 MHz, 00001 = 73.7 MHz, 00010 = 88.5 MHz
// 00011 = 103.2 MHz, 00100 = 118.0 MHz, 00101 = 132.7 MHz
// 00110 = 147.5 MHz, 00111 = 162.2 MHz, 01000 = 176.9 MHz
// 01001 = 191.7 MHz, 01010 = 206.4 MHz, 01011 = 221.2 MHz
mov r1, #0x90000000
add r1, r1, #0x20000
mov r2, #0x0a
str r2, [r1, #0x14]

## Slide 107: Source of Sample Bootloader
// GPDR(GPIO Pin Direction Register) = 0x9004 0004
// PD[27:0] = GPDR[27:0]
// 0 (input), 1 (output)
#define GPIO_DIRECTION 0x0000 00ff
mov r2, #0x90000000
add r2, r2, #0x40000
ldr r1, =GPIO_DIRECTION
str r1, [r2, #0x04]
// GPSR (GPIO pin output set register) = 0x9004 0008
// PS[27:0] = GPSR[27:0]
// 0 (low), 1 (high)
ldr r3, =GPIO_DIRECTION
str r3, [r2, #0x08]

## Slide 108: Source of Sample Bootloader
// GRER - (GPIO Rising-Edge Detect Register) = 0x9004 0010
// RE[27:0] = GRER[27:0]
// 0 (Disable), 1 (set GEDR bit high when rising edge is detected)
ldr r3, =0x00000200
str r3, [r2, #0x10]
// GFER (GPIO Falling-Edge Detect Register) = 0x9004 0014
// FE[27:0] = GFER[27:0]
// 0 (disable), 1 (set GEDR bit high when falling edge is detected)
mov r3, #0x00000000
str r3, [r2, #0x14]
// Set Dynamic Memory.
// DRAM configuration register (MDCNFG) = 0xA000 0000
// MDCAS00 (DRAM CAS waveform rotate register 0 for
DRAM bank pair 0/1) = 0xA000 0004
// MDCAS20 (DRAM CAS waveform rotate register 0 for
DRAM bank pair 2/3) = 0xA000 0020
// MDCAS01 = 0xA000 0008, MDCAS02 = 0xA000 000C
// MDCAS21 = 0xA000 0024, MDCAS22 = 0xA000 0028
// MDCASn0[31:0] = 0xAAAA AA7F
// MDCASn1[31:0] = 0xAAAA AAAA
// MDCASn2[31:0] = 0xAAAA AAAA

## Slide 109: Source of Sample Bootloader
// MDREFR.KnDB2 = 0
// (SDRAM)
// RAS-to-CAS delay = 8 * CPU-clock-period
// CAS-to-CAS delay = 2 * CPU-clock-period
// Delay from SDCLK rising edge to read data
// latching edge = 3* CPU-clock-period
mov r1, #0xA0000000
ldr r2, =0xAAAAAA7F
str r2, [r1, #0x04]
str r2, [r1, #0x20]
ldr r2, =0xAAAAAAAA
str r2, [r1, #0x08]
str r2, [r1, #0x24]
ldr r2, =0xAAAAAAAA
str r2, [r1, #0x0C]
str r2, [r1, #0x28]
// MDREFR (DRAM refresh control register) = 0xA000 001C
// 0 (SLFRSH, KAPD, EAPD, K2DB2, K2RUN, K0RUN, E0PIN)
// 1 (K1DB2, K1RUN, E1PIN, K0DB2)
// DRI[11:6] = 0, DRI[5:4] = 1, DRI[3:2] = 0, DRI1 = 1, DRI0 = 0
// TRASR[3:0] = 0111
ldr r2, =0x00740327
str r2, [r1, #0x1C]

## Slide 110: Source of Sample Bootloader
// MDCNFG (DRAM configuration register) = 0xA000 0000
ldr r2, =0x725c7245
str r2, [r1, #0x00]
// Issue read requests to disabled bank to start refresh.
ldr r1, =0xC0000000
.rept 8
ldr r0, [r1]
.endr
// LED 0 on
// GPIO clear register = GPCR : 0x9004 000c
mov r1, #0x90000000
add r1, r1, #0x40000
ldr r2, =0x00000001
str r2, [r1, #0x0C]
// Set Static Memory.
// MSC0(Static memory control register 0) = 0xA000 0010
// MSC1(Static memory control register 1) = 0xA000 0014
// MSC2(Static memory control register 2) = 0xA000 002C
// SMCNFG(SMROM configuration register) = 0xA000 0030
// MECR (Expansion bus configuration register) = 0xA000 0018

## Slide 111: Source of Sample Bootloader
mov r1, #0xA0000000
ldr r2, =0x4b944b90
str r2, [r1, #0x10]
ldr r2, =0x4b954b94
str r2, [r1, #0x14]
ldr r2, =0x00004b95
str r2, [r1, #0x2C]
ldr r2, =0xafccefcc
str r2, [r1, #0x30]
ldr r2, =0x994a994a
str r2, [r1, #0x18]
// Led 1 on
mov r1, #0x90000000
add r1, r1, #0x40000
ldr r2, =0x00000002
str r2, [r1, #0x0C]
// SDRAM Clear
#define DRAM_BASE_ADDR (0xc0000000)
#define DRAM_SIZE (0x02000000) // 32MB

## Slide 112: Source of Sample Bootloader
ldr r1, =DRAM_BASE_ADDR
mov r2, #0x00000000
ldr r3, =DRAM_BASE_ADDR
add r3, r3, #DRAM_SIZE
1:
str r2, [r1]
add r1, r1, #4
cmp r1, r3
bne 1b
// Led 2 on
mov r1, #0x90000000
add r1, r1, #0x40000
ldr r2, =0x00000004
str r2, [r1, #0x0C]
// Set stack pointer
ldr sp, =STACK_POINT

## Slide 113: Source of Sample Bootloader
// Jump to the C code.
jump_to_c:
b BeforeMain
// handler setting
undefined_instruction:
b undefined_instruction
software_interrupt:
b software_interrupt
abort_prefetch:
b abort_prefetch
abort_data:
b abort_data
not_used:
b not_used
irq:
b irq
fiq:
b fiq

## Slide 114: Source of Sample Bootloader (main.c)
typedef struct {
long terminalSpeed;
long downloadSpeed;
} LOADER_STATUS;
LOADER_STATUS status;
void BeforeMain(void);
void CMain(void);
bool DoPrintfHelp(int argc, char **argv);
#define LOADER_SRAM_BASE (0x00000000)
#define LOADER_DRAM_MAX_SIZE (0x00010000)
#define DRAM_SIZE (0x02000000)
#define LOADER_DRAM_BASE
(DRAM_BASE_ADDR+DRAM_SIZE-LOADER_DRAM_MAX_SIZE)
void BeforeMain(){
register ulong *dest = (ulong *)LOADER_DRAM_BASE;
register ulong *src = (ulong *)LOADER_SRAM_BASE;
register ulong len = LOADER_DRAM_MAX_SIZE / 4;
void (*JumpTo)(void);
while (len--) *dest++ = *src++;
JumpTo = CMain;
JumpTo();
return;
}

## Slide 115: Source of Sample Bootloader
void CMain( ){
int i;
bool autoboot=true;
char cmd[128];
long timeout;
int argc=0;
char *argv[MAX_ARGS];
CMD_TBL *cptr;
#define SERIAL_SPEED 1
#define SERIAL_DOWNLOAD_SPEED 1
// 191 : 1200
// 23 : 9600
// 11 : 19200
// 5 : 38400
// 3 : 57600
// 1 : 115200
status.terminalSpeed = SERIAL_SPEED;
status.downloadSpeed = SERIAL_DOWNLOAD_SPEED;
SerialInit(status.terminalSpeed);
TimerInit();
#ifdef USE_LCD_LOGO
ViewLogo();
#endif

## Slide 116: Source of Sample Bootloader
// ethernet initialization
EthInit(); // scc.c
// wait 10 seconds before starting autoboot.
printf("Autoboot in progress, press any key to stop ");
for (i=0; i<DELAY_BEFORE_BOOT; i++){
timeout = GetTime() + HZ; // 1초간 Delay
printf(".");
while (GetTime()<timeout){
// 시리얼포트로 입력이 있으면 입력값은 무시하고 수동부트 모드
if (UTSR1 & UTSR1_RNE){
UTDR;
autoboot = false;
break;
}
}
if (autoboot==false) break;
}

## Slide 117: Source of Sample Bootloader
// No key was pressed, proceed booting the kernel.
if (autoboot){
printf("Autoboot started.\n");
printf("\nkernel loading...");
MemCpy(
(char *)KERNEL_DRAM_BASE,
(char *)KERNEL_SRAM_BASE,
KERNEL_MAX_SIZE);
printf("Done");
printf("\nramdisk loading...");
MemCpy(
(char *)RAMDISK_DRAM_BASE,
(char *)RAMDISK_SRAM_BASE,
RAMDISK_MAX_SIZE);
printf("Done");
for (cptr=cmdTbl; cptr->cmd; cptr++){
if (!StrCmp(cptr->cmd, "boot")) break;
}
DoBootKernel(cptr, 1, 0);
}

## Slide 118: Source of Sample Bootloader
// Key was pressed, proceed command mode.
printf("\nAutoboot aborted\n");
printf("Type \"help\" to get a list of commands\n");
// the command loop. endless, of course.
for(;;) {
DisplayPrompt(NULL);
// wait an hour to get a command.
GetCommand(cmd, 128, 3600);
if (!cmd || !cmd[0]) continue;
argc = GetArgs(cmd, argv);
for (cptr=cmdTbl; cptr->cmd; cptr++){
if (!StrCmp(argv[0], cptr->cmd)){
(cptr->run)(cptr, argc, argv);
break;
}
}
if (!StrCmp(argv[0], "help") || !StrCmp(argv[0], "?")){
DoPrintfHelp(argc, argv);
} else if (!(cptr->cmd)){
printf("\tUnknown command : %s\n", argv[0]);
}
}
} // The end of CMain

## Slide 119: Source of Sample Bootloader (command.c)
bool DoBootKernel(CMD_TBL *cptr, int argc, char **argv){
#ifndef TINY_LOADER
long addr;
#endif
long opt[2];
void (*theKernel)(int zero, int arch);
if (argc!=1 && argc!=3 && argc!=4){
printf(cptr->usage);
return false;
}
switch (argc){
case 1 : // boot
opt[0] = 0; opt[1] = 0x14;
// KERNEL_DRAM_BASE = 0xC000 8000
theKernel = (void (*)(int, int))KERNEL_DRAM_BASE;
break;
case 3 :
(생략)
printf("\nStarting kernel ...\n\n");
theKernel(opt[0], opt[1]);
return true;
}

## Slide 120: Kernel Configuration

## Slide 121: Configuration Options
Code maturity level options
  Prompt for development and/or incompleter code/drivers
Loadable module support
  enable loadable module support
System type
  (SA1100-based) ARM system type - SA11x0 implementations, include support for TBEL1110
General setup
  support hot-pluggable devices
  Networking support
  System V IPC : +18KB
  Sysctl support

## Slide 122: Configuration Options
General setup
  NWFPE math emulation
  kernel core (/proc/kcore) format (ELF/a.out)
  kernel support for ELF binaries** : +13 KB.
  Timer and CPU usage LEDs
  Timer LED
  CPU usage LED
  Kernel-mode alignment trap handler

## Slide 123: Configuration Options
Block devices
  Loopback device support**
  RAM disk support
  Default RAM disk size (8192)
  Initial RAMS disk (initrd) support
  Flash memory block device support
Networking options
  packet socket**
  Unix domain sockets**
  TCP/IP networking

## Slide 124: Configuration Options
Network device support
  Network device support
  Ethernet (10 or 100Mbit)  Ethernet (10 or 100 Mbit)**
  PPP (point-to-point protocol) support**
  PPP support for async serial ports**
  PPP deflate compression**
  PPP BSD-compress compression
Character devices
  Virtual terminal
  SA1100 serial port support
  Console on SA1100 serial port
  Serial console 115200
  Unix98 PTY support

## Slide 125: Configuration Options
File systems
  /proc file system support
  /dev/pts file system for Unix98 PTYs
  Second extended fs support**
  Network file systems  NFS file system support : +27KB.
Kernel hacking
  Verbos kernel error message
  Verbose user fault messages
  Kernel low-level debugging functions

## Slide 126: File System

## Slide 127: Linux File System Architecture
User process
User process
User process
System Call Interface
Virtual File System Switch (VFS)
msdos
ext2
minix
proc
Buffer Cache
Device Drivers
Disk Controller
User mode
Kernel mode

## Slide 128: File System Structure
Each file is represented by a data structure, called an inode.
Inode : File type, access rights, owners, timestamps, size, pointers to data blocks, link counter

## Slide 129: File System Structure
Directory : structured in a hierarchical tree, contains files and subdirectories
  A file containing a list of entries which contains inode number & file name
Link
  Hard link : used only within a single file system. Can only point on files.
  Symbolic link : file containing a filename. Does not point to an inode. Cross-filesystem symoblic link is possible.

## Slide 130: File System Structure
Device special file
  devices can be accessed via special file. Does not use disk space. Access point to the device driver.
Character special file
  I/O operations in character mode
Block special file
  I/O operations in block mode via a buffer cache function.
I/O request on special file
  forwarded to device driver. Referenced by major number (device type) & minor number (device unit)

## Slide 131: Virtual File System Switch (VFS)
VFS
  Abstraction layer between application program and filesystem
    Provides system calls for file management
    Maintains internal data structures and pass task on to actual file system
  Common interface to various filesystem

## Slide 132: Virtual File System Switch (VFS)
Filesystem supported by VFS
  Disk-based filesystem : manage memory space of local disk parition
    EXT2, MS-DOS, VFAT, NTFS, ISO9660 CD-ROM
  Network-based filesystem : access the filesystem belongs to other computer in network.
    NFS, Coda, AFS, SMB, NCP
  Special filesystem (virtual filesystem) : no use of disk space
    /proc : provide the interface for user to access data structure of kernel
    /dev/pts : support pseudo-terminal of Open Group’s UNIX 98 standard

## Slide 133: /Proc File System
Provide the information on the status of kernel and running processes
Inodes for /proc
  Root : 1
  Others : defined in <linux/proc_fs.h>
Directory structure
  /proc/pid : holding informtion on process-pid
  /proc/loadavg : provide average system load for the last 1, 5, 15 minutes
  /proc/uptime : indicates time in seconds since system start and the time used by idle process
  /proc/meminfo : contains the number of total, used and free bytes of main memory and swap area
  /proc/kmsg : supplies kernel messages which have not been read viad syslog system call
  /proc/version : kernel version information
  /proc/cpuinfo : parameters of the processor
  /proc/pci : occupation of PCI slots
  /proc/self/ : information about the process accessing /proc file system
  /proc/scsi/ : information about SCSI devices
  /proc/malloc : monitoring of kmalloc(), kfree()
  /proc/kcore : core dump of kernel

## Slide 134: /Proc File System
Directory structure (continued)
  /proc/net/ : files that describe Linux network layer
    unix : information on opened Unix domain sockets
    arp : contents of ARP table
    route : routing table
    dev : available network devices
    raw : information about opened RAW sockets
    tcp : information about TCP sockets
    uDP : information about UDP sockets
    snmp : MIB (Management Information Bases) for SNMP protocol
    sockstat : statistics about the sockets
  /proc/modules : information about modules loaded, size and status
  /proc/stat : Linux kernel statistics
  /proc/devices : information about registered device drivers
  /proc/interrupts : the number and names of hardware interrupt received.
  /proc/filesystems : existing file system of kernel
  /proc/ksyms : all symbols exported by kernel
  /proc/dma : DMA channel information

## Slide 135: /Proc File System
Directory structure (continued)
  /proc/sys/ : information controlling kernel algorithms
    kernel
      domainname : system domain name
      filemax : max # of simultaneously opened files
      filenr : # of currently opened files
      hostname : computer name
      inodemax : max # of simultaneously opened inodes
      inodenr : # of currently opened inodes
      osrelease : kernel version
      ostype : operting system name
      panic : timeout after a panic message
      securelevel : security level
      version : compiler information during kernel compilation
    net/ : depends on network configuration
    vm/ : control parameters of memory management processes
      bdflush : control parameters of bd_flush process
      freepages : value of free-page levels
      kswapd : control parameters of kswap daemon
      swapctl : control parameters of swap process

## Slide 136: /Proc File System
Directory structure (continued)
  /proc/ioports : I/O ports occupied via request_region()
  /proc/smp : information on CPUs in SMP systems
  /proc/cmdline : command line passed to kernel at startup
  /proc/mtab : list of currently mounted file systems
  /proc/md : statistics on usage of multiple device driver (CONFIG_BLK_DEV_MD configured)
  /proc/rc : RTC values (CONFIG_RTC configured)
  /proc/locks : current file locks

## Slide 137: Linux File System
 | Minix | Ext | Ext2 | EXT3 | EXT4
Max. FS Size | 64M | 2G | 4T | 32T | 1E
Max. File Size | 64M | 2G | 2G | 2T | 16T
Max. File Name | 14 | 255 | 255 | 254 | 256
Variable Block Size | X | X | 1K~8K |  | 
Minix : 1987, the first file-system of Linux
EXT (extended file system) : 1992. 4, v0.96c
EXT2 : 1993, improved EXT file-system
EXT3 : 2001.11, v.2.4.15, journaling file-system
EXT4 : 2008.12, v2.6.28, pre-allocation, delayed-allocation

## Slide 138: Ext2 File System Structure
Physical structure of filesystem
Structure of block group
Boot Sector
Block Group 1
Block Group 2
... ...
Block Group N
Super Block
Group Descriptors
Block Bitmap
Inode Bitmap
Inode Table
Data Blocks

## Slide 139: Ext2 File System Structure
Block group descriptor (32-bytes)
Directory
  Managed using singly linked list
  Date structure of directory entry
Block bitmap |  | Inode bitmap | 
Inode table |  | # of free blocks | # of free inodes
# of directories | Pad words |  | 
0
7
struct ext2_dir_entry {
unsigned long inode; // inode number
unsigned short rec_len; // length of directory entry
unsigned short name_len; // length of filename
char name[EXT2_NAME_LEN]; // filename
};

## Slide 140: Ext2 File System Structure
Inode (128 bytes)
Type/Permission | UID | File size
Access time |  | Time of creation
Time of modification |  | Time of deletion
GID | Link counter | # of blocks
File attributes |  | Reserved
1st direct block |  | 
…. |  | 
12-th direct block |  | 
1-stage indirect block |  | 2-stage indirect block
3-stage indirect block |  | File version
File ACL (access control list) |  | Directory ACL
Fragment address |  | Reserved
0
7

## Slide 141: EXT2 Library and Tools
Libext2fs : allow user to manipulate the control structure of Ext2 filesystem
  Filesystem-oriented operations
  Directory-oriented operations
  Inode-oriented operations
Tools
  tune2fs : modify filesystem parameters
  e2fsck : repair filesystem consistencies after unclean shutdown
    Phase-1 : inode check
    Phase-2 : directory check
    Phase-3 : directory connectivity check
    Phase-4 : reference count (link count) check for all inodes
    Phase-5 : check the validity of filesystem summary information
  debugfs : examine and change the state of filesystem

## Slide 142: Ramdisk
Ramdisk device
  Use a part of main memory as hard disk
  /dev/ram0, /dev/ram1
Ramdisk image
  File having ramdisk or file system image mounted with “–o” loop option
Ramdisk object
  ELF object file having ramdisk image (generally compressed)

## Slide 143: Loop Device
Loop device
  Virtual device which use a file as file system
  /dev/loop0, /dev/loop1
Initial ramdisk device
  Use loop device as root file system
  After executing /linuxrc program on ramdisk, the file system on the other device is mounted as root file system.
  Even after changing root file system, initial ramdisk device can be accessed through /dev/initrd device.

## Slide 144: Ramdisk Generation
dd if=/dev/zero of=/tmp/fsfile bs=1K count=1000
/sbin/losetup /dev/loop0 /tmp/fsfile
/sbin/mke2fs /dev/loop0
mkdir /mnt/tmp
mount –t ext2 /dev/loop0 /mnt/tm
cd /mnt/tmp
ls

## Slide 145: Module Programming

## Slide 146: Module
Object code (xxx.o) which can be dynamically linked to kernel.
Loading & removing during executing kernel
Event-driven, not sequential processing
Module is executed in kernel mode
Application of module : device driver, file system, network protocol stack

## Slide 147: Kernel Programming
Not use standard C library
  due to speed & size, too large & inefficient for the kernel
Programmed in GNU C, not in strict ANSI C
  Inline function : inline
  Inline assembly : embedding of assembly instructions
  Branch annotation : likely/unlikely
if (unlikely(foo))
……
if (likely(foo))
……
static inline void fooba (…) {…}
asm (….);

## Slide 148: Kernel Programming
No memory protection in kernel
No use of floating point
Small, fixed size stack : 8KB
Synchornization/Concurrency is critical
  due to multiprocessing, asynchronous interrupt request, preemptive
Portability

## Slide 149: Module Programming
Careful for using global variables because the global variables used in module affect the kernel.
Careful for accessing memory because there is no limitation on memory access.
Translate the floating arithmetic into the floating arithmetic.
Careful for using data array & recursive call because the size of kernel stack is limited.
Do not use processor-specific code for portability. Word size and order of storing data (endian) should be considered.

## Slide 150: Module Programming
Interfaces between application, kernel and hardware
Address space
Application
Kernel
H/W
System
Call
return
command
IRQ
User Address Space
Kernel Address Space
PAGE_OFFSET
0xC000 000
3G
1G

## Slide 151: Module Programming
Message output function to standard output device : same as printf function
  For code efficiency, standard C library can not be used in kernel / module.
Input/output device function
printk(LOG_LEVEL const char *pstr);
// LOG_LEVEL : KERN_EMERG, KERN_ALERT, KERN_ERR,
KERN_WARNING, KER_INFO, KERN_DEBUG
// byte-based
unsigned inb (unsigned ioport);
unsigned outb (char value, unsigned ioport);
void insb(unsigned ioport, void *addr, unsigned log count);
void outsb(unsigned ioport, void *addr, unsigned long count);
// halfword(16-bit), word(32-bit)-based
unsigned inw/inl (unsigned ioport);
unsigned outw/outl (char value, unsigned ioport);
void insw/insl(unsigned ioport, void *addr, unsigned log count);
void outsw/outsl(unsigned ioport, void *addr, unsigned long count);

## Slide 152: Module Programming
Data transfer between user space and kernel space
Memory allocation
unsigned long copy_from_user(void *to, const void *from, unsigned long n);
unsigned long copy_to_user(void *to, const void *from, unsigned long n);
// 128~128KB, contiguous physical memory allocation
void *kmalloc(unsigned int len, int priority);
void kfree(void *ptr);
// no limit in size, contiguous virtual memory allocation
void vmalloc(unsigned int len); // for virtual memory
void vmfree(void *ptr);
void *memset(void *s, char c, size_t count);
put_user(data, ptr); // the size of “data” depends on data type of “ptr”
get_user(ptr); // 1, 2, 4 bytes

## Slide 153: Module Programming
Interrupt related functions
Interrupt handler functions
cli(); // clear interrupt
sti(); // set interrupt
// interrupt handler registration
int request_irq(unsigned int irq_no, void(*handler)(int),
unsigned long flags, const char *device);
// interrupt handler release
void free_irq(unsigned int irq_no);
save_flags(unsigned long flag); // save status register
restore_flags(unsigned long flag); // restore status register

## Slide 154: Module Programming
Synchronization
struct wait_queue {
struct tast_struct *task;
struct wait_queue *next;
};
void sleep_on(struct wait_queue **p);
void interruptible_sleep_on(struct wait_queue **p);
void wake_up(struct wait_queue **p);
void wake_up_interruptible(struct wait_queue **p);

## Slide 155: Module Programming
Device driver handling functions
int register_chrdev(unsgined int major, const char *name, struct file_operations *fops);
int register_blkdev(unsgined int major, const char *name, struct file_operations *fops);
int register_netdev(struct net_device *dev);
int unregister_chrdev(unsgined int major, const char *name);
int unregister_blkdev(unsgined int major, const char *name);
int unregister_netdev(struct net_device *dev);

## Slide 156: Module Programming
Data structure for module
  struct module {
  unsigned long size_of_struct; // sizeof(module)
  struct module *next;
  const char *name; // module name
  unsigned long size; // module size
  union { atomic_t usecount; // module usage counter
  long pad; } uc;
  unsigned long flags; // module flags
  unsigned nsyms; // # of exported symbols
  unsigned ndeps; // # of referenced modules
  struct module_symbol *syms; // table of exported symbols
  struct module_ref *deps; // list of referenced modules
  struct module_ref *refs; // list of referencing modules
  int (*init)(void); // initialization method
  void (*cleanup)(void); // cleanup method
  const struct exception_table_entry *ex_table_start; // start of exception table
  const struct exception_table_entry *ex_table_end; // end of exception table
  ……
  };

## Slide 157: Module Programming
Module loading/unloading
  <linux/init.h>
  int init_module(void); // module loading
  void cleanup_module(void); // module unloading
  <linux/init.h>
  #define module_init(x) int init_module(void) { return x(); }
  #define module_exit(x) void cleanup_module(void) { x(); }

## Slide 158: Module Programming
Usage count
  Counting the number of processes using the module.
  Checking whether the module is used or not.
  Related macro
    MOD_INC_USE_COUNT : usage count ++
    MOD_DEC_USE_COUNT : usage count --
    MOD_IN_USE : return TRUE if usage count is not equal to ‘0’
Information about symbols registered in symbol table
  /proc/ksyms
  address + symbol name + version number :
  Ex) c0134a50 register_chardev_R1a5f156e

## Slide 159: Module Programming
Template of module programming
  #include <linux/kernel.h>
  #include <linux/module.h>
  #include <linux/init.h>
  int module_start();
  void module_end();
  EXPORT_NO_SYMBOLS;
  module_init(module_start);
  module_exit(module_end);
  int module_start() { …… }
  int module_end() { …… }

## Slide 160: Module Programming
Compile option
  “c” option : Linker is not called because it will link to kernel directly
  “Wall” option : check all errors and warnings.
  “O” option : protect inline function from trying to make external link.
  “D” option : define symbols and macros. __KERNEL__ (kernel symbol & macro), MODULE (module), LINUX (Linux related)
Usages
  # gcc –c –O –Wall –DMODULE –D__KERNEL__ -DLINUX hello.c

## Slide 161: Version Checking
Make sure that kernel version and module version is same.
Kernel version data of module
  kernel_version[] in <linux/module.h>
Kernel version in kernel itself
  LINUX_VERSION_CODE in < linux/version.h>
    Ex) ver 1.3.5 : 0x10305 (66309), ver 2.4.0 : 0x20400 (132096)
<linux/module.h>
#include <linux/version.h>
static const char __module_kernel_version[] __attribute__((section(".modinfo"))) =
"kernel_version=" UTS_RELEASE;
<linux/version.h>
#define UTS_RELEASE "2.4.0-test5-rmk1-np1"
#define LINUX_VERSION_CODE 132096

## Slide 162: Version Checking
Macro for kernel version checking
  KERNEL_VERSION (vers, rel, seq)
    vers << 16 | rel << 8 | seq
Dependency checking example
<linux/version.h>
#define KERNEL_VERSION(a,b,c) (((a) << 16) + ((b) << 8) + (c))
#ifdef LINUX_KERNEL_CODE <= KERNEL_VERSION(2,4,0)
….do something under ver 2.4.0…….
#else
….do something over ver 2.4.0…….
#endif

## Slide 163: Shell Commands for Module
/sbin/insmod
  Link dynamically to kernel, Require root privilege
/sbin/rmmod
  Remove module from kernel
/sbin/lsmod
  Check state of module
  Same as /proc/modules file
/sbin/depmod
  Check dependency of module
/sbin/modprobe
  Load module and its dependent modules
/sbin/modinfo
  Display information about the module

## Slide 164: Communication between Module and User
Using /dev file system
Using /proc file system
  Virtual file system having information about kernel
How to communicate with module using /proc file system
  Generate new file under /proc directory.
  Use file operation to access /proc file system.
  File registration to /proc file system : create_proc_entry ()
  File deletion from /proc file system : remove_proc_entry ()

## Slide 165: Data Entry Structure of /proc
Data entry structure (proc_dir_entry)
  Define the characteristics of pseudo file generated under /proc directory after module generation.
  struct proc_dir_entry = {
  unsigned short low_ino; // inode value of file
unsigned short name_len; // length of file name
const char *name; // file name generated
mode_t mode; // file access mode
…
struct inode_operation *proc_iops; // file operation
read_proc_t *read_proc; // file pointer for reading
write_proc_t *write_proc; // file pointer for writing
…
};

## Slide 166: Registration &Deletion of /proc Entry
Registration of /proc entry
  create_proc_entry()
Deletion of /proc entry
  remove_proc_entry()
#include <linux/proc_fs.h>
  struct proc_dir_entry (*create_proc_entry)(const char *name, mode_t mode, struct proc_dir_entry *parent)
  name : filename
  mode : access right for file
  parent : location of file generated (if /proc, then NULL)
  void remove_proc_entry(const char *name, struct proc_dir_entry *parent)

## Slide 167: Read & Write of /proc
Function pointer read_proc for reading, write_proc for writing of proc_dir_entry
#include <linux/proc_fs.h>
struct proc_dir_entry *ent;
int proc_read (char *buf, char **start, off_t off, int count, int *eof, void *data);
int init_module() {
ent = create_proc_entry (myfile, S_IRUGO, NULL);
if (ent != NULL) ent->read_proc = proc_read;
}
void cleanup_module() {
remove_proc_entry(myfile, NULL);
}
int proc_read(char *buf, char **start, off_t off, int count, int *eof, void *data) {
int len;
len = sprintf(buf, “hello ! \n”);
return len;
}

## Slide 168: Device Driver

## Slide 169: Linux System Architecture
Network subsystem
Application
System call interface
Virtual Filesystem Switch (VFS)
Buffer cache
Character
device driver
Device interface
Hardware
Block
device driver
Network
device driver

## Slide 170: Device Access Mode
Polling mode
  Periodical checking the status of input/output operation
Interrupt mode
  Cheking the status of input/output operation by using interrupt
Device driver
Device
Process
(I/O Request)
Call
Cmd
Status
Polling
Status
Return
User
Space
Kernel
Space
Polling Mode I/O Operation
Device driver
Device
Call
Cmd
IRQ
Return
Interrupt Mode I/O Operation
Process
(I/O Request)
ISR
ret_from_sys_call
 Bottom half
 Scheduler
Blocked
Resumed

## Slide 171: Device Driver
Device driver
  Consists of data structures & functions used to control I/O devices.
  Device access by user : use the file name of /dev file system
  Device access by kernel : use device driver & major number & minor number of device.
  Upper 8-bit of “i_dev” variable of device file = major number
  Lower 8-bit of “i_dev” = minor number.
Advantages of device driver
  Unified interface of kernel to various types of devices.
  By capsulizing the program code specific to devices as module, it is easy to optimize the kernel size by loading and deleting it dynamically.
  It is easy to add the device : Device manufacturer can add new device without understanding in detail about kernel source code

## Slide 172: Device Driver
Major number
  Interger (0 ~ 255)
  Same major number for same device driver
  Major number of device in use
    include/linux/major.h or /proc/devices
Minor number
  Integer (0 ~ 255)
  Identify the devices whose major number is same.

## Slide 173: Device Type
Character device
  Sequential access in character-base, not use buffer cache.
  Can be accessed by calling system calls (open, close, read, write)
  Reference = “c”
  Can not use seek system call.
  Serial port, console port, mouse, parallel port, etc
Block device
  Random access in block-based, use buffer cache.
  Reference = “b”
  Ram disk, hard disk, cd-rom, etc

## Slide 174: Device Type
Network device
  Packet-based device
    Can not map to a special file
  Use packet transfer functions
    socket(), bind(), listen(), accept(), connect()

## Slide 175: Loading of Device Driver
Registration function : register_xxxdev() in <linux/fs.h>
int register_chrdev(unsigned int major, const char *name, struct file_operations *fops);
int register_blkdev(unsgined int major, const char *name, struct file_operations *fops);
int register_netdev(struct net_device *dev);
- major : major number, if ‘0’, kernel allocates it dynamically
name : device name, /proc/devices.
fops : address of data structure of file operation related to device.
# cat /proc/devices
Character devices:
1 mem
2 pty
3 ttyp
4 ttyS
5 cua
…..
Block devices:
1 ramdisk
3 ide0
7 loop
#

## Slide 176: Device Table
Device table : store device driver name & funtion pointer to its file operations. Index = major number of device driver
#define MAX_CHRDEV 255
struct device_struct {
const char *name;
struct file_operations *fops;
};
static struct device_struct chardevs[MAX_CHRDEV];
#define MAX_BLKDEV 255
static struct {
const char *name;
struct block_device_operations *bdops;
} blkdevs[MAX_BLKDEV];
0
1
2
254
name
fops
Device driver name
File operations
open()
read()
chardevs[255]

## Slide 177: Unloading of Device Driver
Deletion function : unregister_xxxdev()
Device file generation
int unregister_chrdev(unsgined int major, const char *name);
int unregister_blkdev(unsgined int major, const char *name);
int unregister_netdev(struct net_device *dev);
# mknod [device_file_name] [type] [major] [minor]
# mknod /dev/my_dev c 250 1

## Slide 178: Usage Counter of Device Driver
Usage count : the number of usages of device driver
Macro for usage count : defined in <linux/module.h>
  MOD_INC_USE_COUNT : increase current usage count by 1
  MOD_DEC_USE_COUNT : decrease current usage count by 1
  MOD_IN_USE : check whether current usage count is 0 or not
/proc/modules : information about modules in use
# cat /proc/modules
netlink 3180 -1 [ipv6]
floppy 45960 1 (autoclean)
monitor 516 0 (unused)
Module name
# of bytes used
Managed by ‘kerneld’
Usage count
Usage count is not used
Referenced by ‘ipv6’

## Slide 179: File Operations for Device
Data structure of file operation : defined in <linux/fs.h>
struct file_operation {
struct module *owner;
loff_t (*lseek)(struct file *, off_t, int);
ssize_t (*read)(struct file *, char *, size_t, loff_t *);
ssize_t (*write)(struct file *, const char *, size_t, loff_t *);
int (*readdir)(struct file *, void *, filldir_t);
unsigned int (*poll)(struct file *, struct poll_table_struct *);
int (*ioctl)(strut inode *, struct file *, unsigned int, unsigned long);
int (*mmap)(struct file *, struct vm_area_struct *);
int (*open)(struct inode *, struct file *);
int (*flush)(struct file *);
int (*release)(struct inode *, struct file *);
int (*fsync)(struct file *, struct dentry *);
int (*fasync)(int, struct file *, int );
int (*check_media_change)(kdev_t dev);
int (*revalidate)(kdev_t dev);
int (*lock)(struct file *, int, struct file_lock *);
ssize_t (*readv)(struct file *, const struct iovec *, unsigned long, loff_t *);
ssize_t (*writev)(struct file *, const struct iovec *, unsigned long, loff_t *);
};

## Slide 180: File Operations for Device
loff_t (*lseek)(struct file *, off_t, int);
  relocate the position for reading/writing. loff_t = long long (64-bit)
ssize_t (*read)(struct file *, char *, size_t, loff_t *);
  Reading data from device, return the number of bytes read.
ssize_t (*write)(struct file *, const char *, size_t, loff_t *);
  Writing data to device.
int (*readdir)(struct file *, void *, filldir_t);
  Reading directory information. Not used for device driver.
unsigned int (*poll)(struct file *, struct poll_table_struct *);
  Insert current process into waiting queue.

## Slide 181: File Operations for Device
int (*ioctl)(strut inode *, struct file *, unsigned int, unsigned long);
  Call device-dependent control commands.
int (*mmap)(struct file *, struct vm_area_struct *);
  Map device memory to process memory.
int (*open)(struct inode *, struct file *);
  Initialize the device.
int (*flush)(struct file *);
  Write data to device. Used in SCSI device.
int (*release)(struct inode *, struct file *);
  Close device file. Retrun used memory space.
int (*fsync)(struct file *, struct dentry *);
  Write all data in buffer to device.

## Slide 182: File Operations for Device
int (*fasync)(int, struct file *, int );
  Check the device whose FASYNC flas is changed.
int (*check_media_change)(kdev_t dev);
  Only for block device. Used in removable device.
int (*revalidate)(kdev_t dev);
  Manage buffer cache
int (*lock)(struct file *, int, struct file_lock *);
  Lock the file
ssize_t (*readv)(struct file *, const struct iovec *, unsigned long, loff_t *);
  Read data from the buffer
ssize_t (*writev)(struct file *, const struct iovec *, unsigned long, loff_t *);
  Write data to the buffer.

## Slide 183: Usage of File Operations for Device
struct file_operation dvi_fop ={
read : dvi_read,
write : dvi_write,
open : dvi_open,
release : dvi_release
};
ssize_t dvi_read() {
}
ssize_t dvi_write() {
}
int dvi_open() {
}
int dvi_release() {
}

## Slide 184: Blocking I/O
IF device is busy, put the process requesting device access in waiting state till the device is available.
Waiting process
Wake-up process
Interruptible or not : when wake-up, handle the suspended interrupt during waiting state. For the critical part of kernel (wake_up), For device driver (wake_up_interruptible)
#include <linux/sched.h>
void interruptible_sleep_on(struct wait_queue **q);
void sleep_on(struct wait_queue **);
void wake_up_interruptible(struct wait_queue **q);
void wake_up(struct wait_queue **);

## Slide 185: Blocking I/O
Waiting queue
  Linked-list in Kernel 2.4
    Header : wait_queue_head_t
    Entry : wait_queue_t
  Defining waiting queue before use it
    Macro : DECLARE_WAIT_QUEUE_HEAD(wq)

## Slide 186: Blocking I/O
#include <linux/sched.h>
static DECLARE_WAIT_QUEUE_HEAD (wq);
static ssize_t foo_read(struct file *filp, char *buf, size_t len, loff_t *offset) {
printk(KERN_DEBUG “process %d (%s) \n”, current->pid, current->comm);
interruptible_sleep_on(&wq);
printk(KERN_DEBUG “awoken %d (%s) \n”, current->pid, current->comm);
return 0;
}
static ssize_t foo_write(struc file *filp, const char *buf, size_t len, loff_t *offset) {
printk(KERN_DEBUG “process %d (%s) \n”, current->pid, current->comm);
wake_up_interruptible(&wq);
return count;
}

## Slide 187: Interrupt Handler
Interrupt and its device : /proc/interrupts
Interrupt request & release function
Interrupt registration function
  init_module or open
int request_irq(unsigned int irq, void (*handler)(int, void *, struct pt_regs *), unsgined long flags, const char *device, void *dev_id);
void free_irq(unsigned int irq, void *dev_id);
irq : interrupt number
(*handler) : interrupt handler
flags : bit mask for interrupt, -SA_INTERRUPT (fast interrupt),
-SA_SHIRQ (share IRQ among multiple devices)
*device : device name
*dev_id : if interrupt is shared, identify the device

## Slide 188: Interrupt Handler
Interrupt handler can not exchange data with user space.
In case of normal interrupt, we have to handle other interrupts.
Role of interrupt handler
  Remove interrupt pending bit of the device
  Read data from kernel or write data to device for interupt handling
  Wake up the waiting processes

## Slide 189: EX-1 : Character Device Driver
#include <linux/kernel.h>
#include <linux/module.h>
#include <linux/init.h>
#include <linux/config.h>
#include <linux/sched.h>
#include <linux/string.h>
#include <linux/malloc.h>
#include <linux/delay.h>
#include <linux/errono.h>
#include <linux/types.h>
#include <asm/hardware.h>
#include <asm/uaccess.h>
#include <asm/irq.h>
#include <asm/param.h>
#include “Gpio_int.h”
#define END_OF_FILE -1
static DECLARE_WAIT_QUEUE_HEAD(device_wait_queue);
static int device_init(void);
static void device_exit(void);
static int device_open(struct inode *, struct file *);
static int device_release(struct inode *, struct file *);
static ssize_t device_read(struct file *, char *, size_t, loff_t *);
static ssize_t device_write(struct file *, const char *, size_t, loff_t *);
static int device_ioctl(struct inode *, struct file *, unsigned int, unsigned long);
static void gpio_irq_handler(int, void *, struct pt_regs *);
static unsigned int nfalling_edge;
static struct gpio_irq_stat *buffer_queue;
static int front, rear;

## Slide 190
static struct file_operations device_fops = {
open : device_open,
read : device_read,
write : device_write,
ioctl : device_ioctl,
release : device_release };
static int device_init(void) {
if(register_chrdev(MAJOR_NUMBER, “gpio_int”, &device_fops) <0 ) {
printk(“Device registration failed \n”); return MAJOR_NUMBER;
}
printk(DEVICE_NAME “:device is with Major number = %d\n”, MAJOR_NUMBER); return 0;
static void device_exit(void) {
unregister_chrdev(MAJOR_NUMBER, “gpio_int”);
}

## Slide 191
static int device_open(struct inode *inode, struct file *filp) {
int nRet;
buffer_queue = (struct gpio_irq_stat *) kmalloc (BIFFER_SIZE * sizeof(struct gpio_irq_stat),
GFP_KERNEL);
rear = front = 0;
nfalling_edge = 0;
GPDR &= ~(GPIO_GPIO0);
set_GPIO_IRQ_edge(GPIO_GPIO0, GPIO_FALLING_EDGE);
nRet = request_irq(IRQ_GPIO0, gpio_irq_handler, SA_INTERRUPT, “GPIO) IRQ”, (void *)0);
if(nRet) {
printk(“GPIO_interrupt : can’t get GPIO0 IRQ”); return -EAGAIN;
}
MOD_INC_USE_COUNT; return 0;
}
static int device_release(struct inode *inode, struct fiel *filp) {
kfree(buffer_queue);
free_irq(IRQ_GPIO0, (void *)0);
MOD_DEC_USE_COUNT; return 0;
}

## Slide 192
static ssize_t device_read(struct file *filp, char *buf, size_t count, loff_t *fops) {
int nCopytoBuf = 0;
char pre_buf[1024];
int len = 0;
int I, nCnt;
if(!access_ok(VERIFY_WRITE, buf, count)) { printk(“buffer is empty\n”); return -EFAULT; }
memset(pre_buf, 0, 1024);
if(front == rear) {
printfk(“buffer is empty\n”);
if(flip->f_flags & O_NONBLOCK) return -EAGAIN;
else interruptible_sleep_on(&device_wait_queue);
}
if(front < rear) nCnt = rear - front;
else nCnt = rear + BUFFERSIZE - front;
for(I=0; I<nCnt; nCopytoBuf += len, I++) {
len = sprintf(pre_buf+nCopytoBuf, “irg=%d, jiffies=%ld, edge=%d\n”,
buffer_queue[front].bit_number, buffer_queue[front].irq_time,
buffer_queue[front].nfalling_edge_stat);
front = (front+1)% BUFFER_SIZE;
}
__copy_to_user(buf, pre_buf, nCopytoBuf); return nCopytoBuf;
}

## Slide 193
static ssize_t device_write(struct file *filp, const char *buf, size_t count, loff_t *fops) {
int target_bit = 0;
unsigned long bitstate, flags;
save_flags(flags);
cli();
printk(“target bit : %d\n”, target_bit);
GPDR != GPIO_GPIO(target_bit);
bitstate = (GPLR & GPIO_GPIO(target_bit)) >> target_bit;
printk(“Value of %d (before toggle) : %ld\n”, target_bit, bitstate);
if(bitstate) {
printk(“Clear\n”);
GPCR = GPIO_GPIO(target_bit);
} else {
printk(“Set \n”);
GPSR = GPIO_GPIO(target_bit);
}
bitstate = (GPLR & GPIO_GPIO(target_bit)) >> target_bit;
printk(“Value of %d (after toggle) : %ld\n”,target_bit,bitstate);
restore_flags(flags);
GPDR &= ~(GPIO_GPIO(target_bit));
return count;
}

## Slide 194
static void gpio_irq_handler(int irq, void *dev_id, struct pt_regs *regs) {
nfalling_edge++;
if(front == (rear+1) %BUFFER_SIZE) {
printk(“Buffer is full \n”); return;
} else {
buffer_queue[rear].bit_number = irq;
buffer_queue[rear].irq_time = jiffies;
buffer_queue[rear].nfalling_edge_stat = nfalling_edge;
rear = (rear+1) % BUFFER_SIZE;
}
wake_up_interruptible(&device_wait_queue);
}
EXPORT_NO_SYMBOLS;
module_init(device_init);
module_exit(device_exit);

## Slide 195
int main() {
int fd;
fd = open(“/dev/gpio_int”,O_RDWR);
gpio_read(fd);
gpio_write(fd);
}
Void gpio_read(int fd) {
len = read(fd, str, 1024);
}
Void gpio_write(int fd) {
len = write(fd, (int *)1,sizeof(int));
}

## Slide 196: Ex-2 : Device Driver for LED
Step-1 : Memory map 확인
(include/asm-arm/mach/map.h)
struct map_desc {
unsigned long virtual;
unsigned long physical;
unsigned long length;
int domain:4,
port_read:1,
port_write:1,
cacheable:1,
bufferable:1;
};

## Slide 197
(arch/arm/mm/map-sa110.c)  arch/arm/mach-sa1100/generic.c, lart.c
#define SA1100_STD_IO_MAPPING \
/* virtual physical length domain r w c b */ \
{ 0xe0000000, 0x20000000, 0x04000000, DOMAIN_IO, 1, 1, 0, 0 }, /* PCMCIA0 IO */ \
{ 0xe4000000, 0x30000000, 0x04000000, DOMAIN_IO, 1, 1, 0, 0 }, /* PCMCIA1 IO */ \
{ 0xe8000000, 0x28000000, 0x04000000, DOMAIN_IO, 1, 1, 0, 0 }, /* PCMCIA0 attr */ \
{ 0xec000000, 0x38000000, 0x04000000, DOMAIN_IO, 1, 1, 0, 0 }, /* PCMCIA1 attr */ \
{ 0xf0000000, 0x2c000000, 0x04000000, DOMAIN_IO, 1, 1, 0, 0 }, /* PCMCIA0 mem */ \
{ 0xf4000000, 0x3c000000, 0x02000000, DOMAIN_IO, 1, 1, 0, 0 }, /* PCMCIA1 mem */ \
{ 0xf8000000, 0x80000000, 0x02000000, DOMAIN_IO, 0, 1, 0, 0 }, /* PCM */ \
{ 0xfa000000, 0x90000000, 0x02000000, DOMAIN_IO, 0, 1, 0, 0 }, /* SCM */ \
{ 0xfc000000, 0xa0000000, 0x02000000, DOMAIN_IO, 0, 1, 0, 0 }, /* MER */ \
{ 0xfe000000, 0xb0000000, 0x02000000, DOMAIN_IO, 0, 1, 0, 0 } /* LCD + DMA */
static struct map_desc tbel1110_io_desc[] __initdata = {
#ifdef CONFIG_SA1100_TBEL1110
{ 0xd0000000, 0x00000000, 0x01000000, DOMAIN_IO, 1, 1, 0, 0 }, /* Flash bank 0 */
{ 0xd8000000, 0x18000000, 0x00800000, DOMAIN_IO, 1, 1, 0, 0 }, /* Ethernet */
SA1100_STD_IO_MAPPING
#endif
};

## Slide 198
-> check kernel space & user space
(include/asm-arm/arch-sa1100/memory.h)
/* Page offset: 3GB */
#define PAGE_OFFSET (0xc0000000UL)
PAGE_OFFSET 의 위는 kernel space (1GB), 아래는 user space (3GB) 로 사용.

## Slide 199
Step-3 : Device driver programming
#include <linux/ioport.h>
#include <asm/uaccess.h>
#include <linux/module.h>
#include <linux/fs.h>
#include <asm/io.h>
#define LEDPORT_MAJOR 0
#define LEDPORT_NAME “LED PORT”
#define LEDPORT_MODULE_VERSION “V1.0”
#define LEDPORT_ADDR 0xf1600000
#define LEDPORT_ADDR_RANGE 1
static int ledport_usage = 0;
static int ledport_major = 0;

## Slide 200
int ledport_open(struct inode *minode, struct file *mfile) {
if(ledport_usage !=0) retrun –EBUSY;
MOD_INC_USE_COUNT;
ledport_usage = 1;
return 0;
}
int ledport_release(struct inode *minode, struct file *mfile) {
MOD_DEC_USE_COUNT;
ledport_usage = 0;
return 0;
}
ssize_t ledport_write_byte(struct fille *inode, const char *gdata, size_t length,
loff_t *off_what) {
unsigned char *addr;
unsigned char c;
get_user(c, gdata);
addr = (unsigned char *)(LEDPORT_ADDR);
*addr = c;
return length;
}

## Slide 201
static struct file_operations led_fops = {
write : ledport_write_byte,
open : ledport_open,
release : ledport_release,
};
int init_module(void) {
int result;
result = register_chrdev(LEDPORT_MAJOR, LEDPORT_NAME, &led_fops);
if(result <0) {
printk(KERN_WARNING”can’t get any major \n);
return result;
}
ledport_major = result;
if(check_region(LEDPORT_ADDR,LEDPORT_ADDR_RANGE))
request_region(LEDPORT_ADDR,LEDPORT_ADDR_RANGE,LEDPORT_NAME);
else
printk(KERN_WARNING”Can’t get IO region 0x%x\n”,LEDPORT_ADDR);
printk(“init module, ledport major number : %d\n”,result);
return 0;
}

## Slide 202
void cleanup_module(void) {
release_region(LEDPORT_ADDR, LEDPORT_ADDR_RANGE);
if(unregister_chrdev(ledport_major,LEDPORT_NAME))
printk(KERN_WARNING”%s driver cleanup failed \n”,LEDPORT_NAME);

## Slide 203
Step-4 : Test program
#include <stdio.h>
#include <stdlib.h>
#include <unistd.h>
#include <sys/types.h>
#include <sys/stat.h>
#include <fcntl.h>
int main(int argc, char **argv) {
int dev;
char buff;
if(argc <= 1) {
printf(“please input parameter \n”); return –1;
}
dev = open(“/dev/ledport”,O_WRONLY);

## Slide 204
if(dev != -1) {
if(argv[1][0]==‘0’)&&(argv[1][1]==‘x’||argv[1][1]==‘X’))
buff = (unsigned char)strtol(&argv[1][2],NULL,16);
else
buff = atoi(argv[1]);
write(dev, &buff, 1);
close(dev);
} else {
printf(“Device open ERROR\n”); exit(-1);
}
return 0;
}

## Slide 205: Makefile Generation
(Makefile)
CC = arm-linux-gcc
KERNLEDIR = /usr/local/linux
INCLUDEDIR = -l$(KERNELDIR)/include –l./
CFLAGS = -D__KERNEL__ -DMODULE –Wall –O2 –l$(INCLUDEDIR)
MODULE_OBJS = ledport.o
MODULE_SRCS = ledport.c
TEST_TARGET = test
TEST_OBJS = test.o
TEST_SRCS = test.c
All: $(MODULE_OBJS) $(TEST_TARTGET)
$(MODULE_OBJS) :
$(CC) $(FLAGS) –c $(MODULE_SRCS)
$(TEST_TARGET) : $(TEST_OBJS)
$(CC) $(CFLAGS) $(TEST_OBJS) –o $@

## Slide 206: Compile & Execution
$ make
; ledport.o, test.o, test file generation
$ insmod ledport.o
Using ledport.o
init module, ledport major number : 253
$ mknod /dev/leport c 253 0
; special device file generation
$ ./test 0xaf
; execution

## Slide 207: Q&A