## Slide 1: IoT Practice-III Raspberry Pi 3 B as IoT Gateway

## Slide 2: Why Raspberry Pi 3 B ?
It is a shortcut of experiencing embedded system.
Can be used as a practical product in well-defined operation condition.
  No problem at indoor application.
Use as the monitoring terminal of solar-cell monitoring system installed at outdoor open space.

## Slide 3: What’s Raspberry Pi 3 B ?
32-bit CPU board
  CPU : Broadcom’s BCM2837
    Quad Core 64-bit CPU @ 1.2GHz
  1GB RAM
  On-board : BCM43438 wireless LAN + Bluetooth Low Energy (BLE)
    100 Base Ethernet
  40-pin extended GPIO
  4 USB 2 ports
  4 Pole stereo output and composite video port
  Full size HDMI
  CSI camera port for connecting a Raspberry Pi camera
  DSI display port for connecting a Raspberry Pi touchscreen display
  Micro SD port for loading your operating system and storing data
  Power supply : Micro USB power source up to 2.5A
Raspberry Pi’s OS
  Raspbian

## Slide 4: What’s should I do for Raspberry Pi ?
Make RP be ready to use !  Set up RP
  Just follow the instruction of the following link step-by-step.
https://projects.raspberrypi.org/en/projects/raspberry-pi-setting-up
Materials required.
RP 3 B
USB power adaptor
MicroSD card
Memory card reader
Host PC
Monitor, Keyboard, Mouse
HDMI cables
Ethernet cable or WiFi dongle

## Slide 5: What’s should I do with Raspberry Pi ?
Use as IoT gateway
  Configuration of IoT Gateway
Host Computer
WoW Kit
USB
SPI
Raspberry Pi 3 B
WiFi
Module
Router
PuTTY (Terminal Emulator)
IoT Cloud
(IoTMakers)
OS + App
Sensor
Local DB
Master DB
IoT Gateway
IoT Device

## Slide 6: What kind of task can I do at IoT Gateway ?
IoT Gateway
  Make a kind of bridge which provides high-speed communication channel, wide bandwidth, additional services for data collecting, storing, analyzing.
Data processing engine(special SW module)
  Data analysis
  Data compression
  AI engine (?)

## Slide 7: LAB : Interworking of IoT Device/Gateway/Cloud
  Test the operation of sending the measured value of vibration sensor to IoT cloud through IoT gateway. The source codes for WoW Kit and Raspberry required for this scenario, will be given. Also, the settings of IoT cloud will be already configured by our staff. Please follow each step as the bellow.
    STEP-1 : Make a group of 3~4 persons.
    STEP-2 : Choose one person as the owner of IoT gateway,
    then the rest will be the owners of IoT devices.
    STEP-3 : Make sure all connections are established.
    STEP-4 : Check the console of IoT gateway & the operation of IoT cloud.
IoT Gateway
IoT Device
IoT Cloud
Vibration Sensor
IoT Device
IoT Device
IoT Device
WiFi
WiFi
Vibration Sensor
Vibration Sensor
Vibration Sensor
Up to 30 IoT devices can be connected to IoT gateway simultaneously
Local DB in IoT gateway consists of time-stamped files, one for a day per each device.

## Slide 8: LAB-1 : IoT Gateway
Packet format for this Lab.
Preamble
Preamble (1) : 0xA5, start of frame (SOF).
Source ID (1) : Identifier of data source. Unsigned integer(range : 10~255, <10 : reserved)
Length (1) : the size of payload in byte. Unsigned integer(0~255)
Source ID
Length
Payload (data)

## Slide 9: Q&A